## Slide 1: Spirometer Software
Olga Neyman
Team mates: Jessie Butts, Abby Cohen
Client: Dr. Klaesner

## Slide 2: Background
Growing concern about non-communicable respiratory diseases
Chronic obstructive pulmonary disease is the only leading cause of death increasing in prevalence worldwide
Notes: Other respiratory diseases
COPD, asthma, etc.

## Slide 3: What is a Spirometer?
Device that measures the volume of air expired and/or inspired
Outputs flow-volume curve and parameters like the forced expiratory volume in 1 second and peak expiratory flow
Spirometer. (Cosmed)
Notes: http://www.cosmed.com/index.php?option=com_content&view=article&id=257&Itemid=125&lang=en

## Slide 4: Flow-Volume Curve
1
(Adapted from Wikipedia)
Notes: FEV1/FVC = 75-80%

## Slide 5: Existing Solutions
Volume-displacing Spirometers:
  Water seal spirometer
  Bellows spirometer
Flow Sensing Spirometers:
  Pneumotach spirometer
    US 5,357,972, US 2,929,248
  Thermistor spirometer
    US 4,993,269
  Turbine spirometer
    US 7,618,235
  Ultrasonic spirometer
    US 5,647,370
Adult Disposable Mouthpiece (Micro Medical, 2011)
Notes: Commercial one

## Slide 6: Need
  80% of developing countries lack access to spirometry equipment – World Health Organization
  Factors like smoking and use of biomass fuels are increasing prevalence of respiratory diseases
Notes: Hindrances- cost, access to doctors, equipment needs to be calibrated, disposable mouthpieces

## Slide 7: Addressing the Need
  WashU Design Team developed a low-cost spirometer
Uses a fluidic oscillator
Audible oscillations occur
Frequency of the oscillations is proportional to the velocity of the air
Low-cost spirometer

## Slide 8: Existing Solutions: Non-Market Approaches
Patent on spirometer with fluidic oscillator
  Uses pressure sensors
    US 8,136,413
Patents on sensors that measure a signal from a fluidic oscillator
  Velocity, microphone, piezoelectric, piezoresistive, capacitive, optoelectric, strain-stress responsive, magnetoresistive sensors
  US 8,091,434, US 3,690,171, etc.

## Slide 9: Need: The Remaining Problem
The low-cost spirometer lacks an optimized sensor and fully-functional software

## Slide 10: Scope
Identify a sensor to pick up the audio signal from the fluidic oscillator
Interface the sensor between the existing hardware and a computer
Design software with a web-based user-friendly interface to read and process the audio signal
Output spirometry curves and parameters
Notes: Process: isolate dominant frequencies, filter, perform calculations
-compare to predicted values
Make more concise
Debate further

## Slide 11: Selected Design Requirements: Sensor
Specification | Desired Value
Cost | <5$
Frequency Response | 0Hz -1 kHz
Type | Noise Cancelling
Signal-to-Noise Ratio | > 60 dB
Directionality | Unidirectional
Shape | Circular
Dimensions | 
Diameter | 0.16 cm– 1.27 cm
Height | < 2.5 cm
Notes: 60 – common in literature
Title columns

## Slide 12: Selected Design Requirements: Software: Functional
Specification | Desired Value
User access | Free access- 24/7
Required patient information | age, gender, height, ethnicity, weight
Maneuver supported | FVC and FEV1 maneuver
Display of data acceptability and data troubleshooting | Display success of maneuver
Notes: Add accuracy

## Slide 13: Selected Design Requirements: Software: Signal Processing
Specification | Desired Value
Data/Web interaction | Store and forward
File Size | 1.7 MB-17 MB
Sampling Rate | 1750 Hz
Signal processing | Noise cancelling
max frequency/ Nyquist = 700 Hz
To prevent aliasing:
Bit Depth = 24 bits/sec
Sample Rate = 48kHz – 192kHz
Recording Length = 6-15 sec
Channels = 2
Notes: Sample rate calculation
File size calculation
Sensor hooked t ocomputer. Computer saves at sampling rate of 48-192. Uploaded as such
File size before sample rate
Sample rate -> nyquist

## Slide 14: Selected Design Requirements: Software: Results
Specification | Desired Value | 
Reference values | NHANES3 | 
Values calculated from data | FVC FEV1 FEV6 Change between tests | Expiration time FEV1/FVC FEV1/FEV6 FEF25-75% FEFX%
Graphs compiled from data | Flow-volume curve, Volume-time curve | 

## Slide 15: Selected Design Requirements: Software: ATS Standards
Accuracy and Precision | 
Specification | Desired Value
FVC Accuracy | +-3% (+-3.5% if using a calibration syringe)
FEV1 | +-3%
FEF25-75% Accuracy | +-5%
Reproducibility | Largest FVC and FEV1 within 150 mL of next
Notes: ATS standards – accuracy/precision

## Slide 16: Preliminary Design Schedule
Tasks | 5-Sep | 12-Sept | 19-Sept | 24-Sept | 1-Oct | 8-Oct | 15-Oct | 22-Oct | 29-Oct | 5-Nov | 12-Nov | 19-Nov | 28-Nov | 5-Dec | 11-Dec
Project Initiation |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Project Selection |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Define Problem |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop Project Plan |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Project Scope |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Become Informed |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Preliminary Oral Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Preliminary Written Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Create Class Webpage |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Design Web App |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Hardware analysis |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Develop GUI |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Progress Oral Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Progress Written Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Interface Analysis |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Web App Implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Software troubleshooting |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Oral Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Final Written Report |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Project Poster |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 17: Organization of Team Responsibilities
Jessie: Hardware
  Sensor
  Hardware /computer interface
  Final Oral Report
  Olga: Backend software development
  Analysis coding and signal processing
  Preliminary Oral Report
  Abby: Frontend development
  Server/ client interface
  Progress Oral Report

## Slide 18: Works Cited
Flow-Volume-Loop. Digital image. Wikipedia. N.p., n.d. Web. 24 Sept. 2012. <http://en.wikipedia.org/wiki/File:Flow-volume-loop.png#filelinks>.
Global Status Report on Noncommunicable Diseases 2010. Geneva, World Health Organization
Micro Medical. (2007). Adult Disposable Mouthpieces. Retrieved September 19, 2012, from Micro Medical: Consumables: http://www.micromedical.co.uk/downloads/pdf/consumables.pdf
Miller, M.R. "Standardization of Spirometry." American Thoracic Society, 2005. Web. <http://www.thoracic.org/statements/resources/pfet/PFT2.pdf>.
PC Based USB Spirometer. Digital image. COSMED Pulmonary Function Equipment. N.p., n.d. Web. 24 Sept. 2012. <http://www.cosmed.com/>.

## Slide 19: Questions?